# RESTful service
The RESTful services are exposed by salsa-engine service when running. These services contain 3 types of API to support different stakeholders:
- Application structure API: with primitive management operations to support normal user or using in web page to interact with users.
- Elasticity controller API: with some advanced operations for SYBL
- Salsa-pioneers API: support salsa-pioneer or others configuration agents in distributed orchestration of configuration process.
# Application structure API
Nr.	RESTful API: /salsa-engine/rest/				Description
	Type	Resource URL	Consumes	Produces
1	PUT	/services/{serviceName}	MULTIPART_FORM_DATA		Deploy the whole app that is described in TOSCA
2	PUT	/services/xml	XML		Submit TOSCA and deploy
3	POST	/services/{serviceId}/redeploy			Undeploy and deploy again
4	DELETE	/services/{serviceId}			Remove service
5	POST	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instance-count/{quantity}			Deploy more a number of service unit
6	DELETE	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instances/{instanceId}			Delete a specific instance
7	DELETE	/services/{serviceId}/nodes/{nodeId}/instances/{instanceId}/metadata			Unmanage an instance by removing its metadata only.
8	GET	/services/{serviceId}			Get the deployment structure of the app
9	GET	/services/tosca/{serviceId}			Get the enriched TOSCA
10	POST	/services/{serviceId}/topologies/{topologyId}			Deploy one topology of the app
11	DELETE	/services/{serviceId}/topologies/{topologyId}			Undeploy one topology
12	DELETE	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}			Undeploy all instance of one service unit

# Elasticity controller API

Nr.	RESTful API: /salsa-engine/rest/				Description
	Type	Resource URL	Consumes	Produces
1	POST	/services/{serviceId}/nodes/{nodeId}/scaleout			Scale out one instance
2	POST	/services/{serviceId}/nodes/{nodeId}/scalein			Scale in one instance
3	POST	/services/{serviceId}/vmnodes/{ip}/scalein			Scale in at infrastructure level with the input is the IP of the VM
4	POST	/services/{serviceId}/vmnodes/{ip}/scaleout			Scale out at infrastructure level.
5	GET	/services/tosca/{serviceId}/sybl		XML	Export the deployment structure as SYBL format

# Salsa-pioneer API

Nr.	RESTful API: /salsa-engine/rest/				Description
	Type	Resource URL	Consumes	Produces
1	GET	/health			Check salsa-engine availability
2	POST	/services/{serviceId}/topologies/{topologyId}	XML		Add metadata
3	POST	/services/{serviceId}/topologies/{topologyId}/tosca	XML		Add metadata from TOSCA
4	PUT	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instances/{instanceId}			Deploy a new instance
5	POST	/services/{serviceId}/topologies/{topologyId}/relationship			Add a new relationship to the topology
6	POST	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instance-counter/{value}			Update the counter for an instance which is used for generating instance ID
7	POST	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instance-metadata			Add instance metadata of already exisitng instance but not managed.
8	POST	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instances/{instanceId}/capability			Update instance capability and shared properties
9	POST	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instances/{instanceId}/properties			Update unit properties after configuration
10	POST	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instances/{instanceId}/state/{value}			Update state of the configuration
12	GET	/services/{serviceId}/topologies/{topologyId}/nodes/{nodeId}/instances/{instanceId}/requirement/{reqId}			Get the shared value of a requirement during the configuration
13	POST	/services/{serviceId}/nodes/{nodeId}/instances/{instanceId}/action_queue/{actionName}			Put an action in a queue to be executed by a pioneer.
14	POST	/services/{serviceId}/nodes/{nodeId}/instances/{instanceId}/action_unqueue			Unqueue an action after a pioneer claim the command and will execute it.
15	POST	/log	PLAIN_TEXT		Pioneer send a log message to salsa-engine
16	GET	/artifacts/pioneer/{fileName}		APPLICATION_OCTET_STREAM	Bootstrap script can get the pioneer artifact from salsa-engine